This document describes how a sensor node is to send data to a collector node.

Collector can be setup multiple ways;
1. Parity bits
2. Manchester encoding
3. Parity bits with handshaking
4. Manchester encoding with handshaking

The setup of the collector will define how the sensor node's data will be encoded, but all data follows the following format:

:01<id><value><checksum>
The collector is a device type :01, this is what any collectors in the area will be looking for.
The <id> is the id of the node and active sensor as described in id systems
The <value> is the reading from the active sensor.
The <checksum> is a checksum calculated in the following way:
checksum = (id + value*x)/y; where x and y are passcodes. The collector will have the same passcode and preform the same calculation, giving a degree of verification, as well as a data integrity check.

In Manchester encoding; each byte is split into a bit array before being sent. Then, after each bit, either a 1 or 0 must be added, a 1 is the preveos bit was a 0, and a 0 is the previous bit was a 1. This effectly creates 2 bytes, on the standard package is send as 6 bytes after the pramble.